## Slide 1
FutureSpace
Movistar Service Intelligence
Three use cases, in depth
Predicting node failures · predicting per-customer degradation · detecting faults today's tools miss — with the data each one needs, and how Structural Intelligence solves it.
Prepared for the Telefónica engagement · Future Space SA
Notes: Title. Frame it immediately as use-case led: three concrete things we can do for Telefónica, each with the exact data fields it needs and how Structural Intelligence solves it. Depth over breadth.

## Slide 2
STRUCTURAL INTELLIGENCE
What it is — and why it's different
An AI that reasons on physical rules and network topology, not on large labelled histories. It reads a fault as a “shape” on the service graph, so it learns from little data and is ideal for critical infrastructures where data is scarce or sensitive.
KEY BENEFITS FOR TELEFÓNICA
⏱
Early prediction
Detects degradation of STBs, routers and service before the customer notices or calls.
○
No mass labelling
Less reliance on long data-labelling projects — starts with what already exists.
→
Minimal integration
Can start offline on already-stored data; low initial complexity.
✓
Concrete example: predicting the degradation of TV set-top boxes (pixelation, quality loss) with ≈ 1 month of historical data — without a custom labelled dataset.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N1

## Slide 3
THE ONE IDEA THE USE CASES REST ON
A fault is a shape on the graph — that is how we localize it
Per-layer dashboards can't explain a customer's experience, because the experience is a property of the whole path, not any one layer.
Structural Intelligence models the ecosystem as one graph — customers, devices, routers, access nodes, core paths, CDN edges — and reads the shape of who-is-affected-sharing-what to place the fault in the layer it lives in.
The richer the graph, the sharper the attribution. Every use case that follows is an application of this one mechanism.
Home fault
alone
Access node fault
a cluster on one node
Core fault
nodes along a path
Content / CDN fault
one source, many nodes
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 2
Notes: The one concept the room must accept before the use cases: a customer's experience is a property of the whole path, so a fault shows up as a shape on the graph. A home fault is alone; an access fault is a cluster on one node; a core fault is nodes along a path; a content fault is one source across many nodes. Reading that shape is how we localize. Every use case is an application of this.

## Slide 4
THE DATA FOUNDATION
What each layer provides — and what we have today
Every use case draws on a defined subset of these layers. The tag shows what is available now versus what requires a new integration with Telefónica.
LAYER
WHAT IT PROVIDES
STATUS
Set-Top Box
Playback & error events, reboots, app behaviour, device & firmware ID
TODAY
Home / Router & Wi-Fi
Router events, Wi-Fi quality, in-home gateway telemetry
TODAY
Customer & household
Device-to-account mapping, household grouping
TODAY
Geography & topology
Device location; which access node / aggregation point a device sits behind
INTEG.
Access network
Line attenuation/noise, local aggregation health
INTEG.
Core network
Transport load, congestion, multicast health along paths
INTEG.
CDN / platform
Edge-cache & origin health, encoder/platform status per content source
INTEG.
Available today
Requires integration with Telefónica
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 3
Notes: The data foundation. Walk the layers quickly. Set-top box, home/router and customer/household are available today; topology, access, core and CDN/platform need integration with Telefónica. Each use case names the subset it draws on — this is the data-assumptions discipline from the MoM (Suman's action item: define data requirements).

## Slide 5
WHAT MAKES IT A GRAPH, NOT A DASHBOARD
Graph construction & service-path data
Events tell us what happened. Path identity and explicit relationships tell us what 2,000 affected customers share — the path, the content, the multicast group, the encoder, or the segment. That commonality is the attribution.
STB
→
Household
→
ONT
→
OLT
→
Aggreg.
→
BNG / Core
→
CDN Edge
→
Content
Every customer is a path through this chain — model the chain explicitly and a fault's location falls out of the structure.
GRAPH CONSTRUCTION — every entity & relationship
entity_id / entity_type node identity & kind
parent_entity / child_entity the edges of the graph
relationship_type STB→Household→ONT→OLT→…
relationship_start / end time-valid topology
link_capacity / confidence edge weight & certainty
PATH IDENTITY — the commonality fields
path_id the end-to-end service path
content_id / channel_id which content / channel
multicast_group_id the IPTV multicast group
route_id / ecmp_path the core route taken
cdn_edge_id / encoder_id the serving edge & encoder
Without explicit relationship and path fields you have labels, not a graph — these are what a traditional observability platform cannot offer.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 4
Notes: Graph construction & service-path data — the structural centrepiece, added after a network-architect review. The point to land: events tell us what happened, but PATH IDENTITY and explicit RELATIONSHIPS tell us what 2,000 affected customers share. Walk the service path (STB→Household→ONT→OLT→Aggregation→BNG/Core→CDN Edge→Content). Then the two field cards: graph construction and path identity. Without these you have labels, not a graph — this is what a traditional observability platform cannot do.

## Slide 6
USE CASE 1 — NETWORK NODES
Predict a node failure before it spreads — and say what to do
01
THE PROBLEM TODAY
Faults at an access node or aggregation point surface as scattered, unexplained complaints — pixelation and freezes across nearby homes. By the time they correlate, many homes are already degraded and the operator is dispatching technicians to the wrong place.
WHAT WE DELIVER
We detect the early structural signature of a node fault as it begins to form, name the exact node, and recommend the specific corrective action — before the wave of complaints arrives.
DATA THIS USE CASE NEEDS, BY LAYER
Set-Top Box playback/error events, reboots
TODAY
Home / Router to rule out in-home causes
TODAY
Topology device → access node mapping
INTEG.
Access net line/aggregation health
INTEG.
Core transport load on the path
INTEG.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 5
Notes: UC1 overview — network nodes. The problem: node faults surface as scattered pixelation/freeze complaints and wrong-place dispatches. The promise: detect the early structural signature, name the exact node, recommend the fix before the complaint wave. The next two slides are the data depth.

## Slide 7
USE CASE 1 — HOW IT'S SOLVED
From scattered events to a named node and a fix
1
Stream the signals
Per-device playback errors, freezes and reboots flow in continuously and are scored against each device's own baseline.
→
2
Find the shared structure
Affected devices are placed on the graph. When pixelation-type events concentrate on devices sharing one access node or path, that co-movement is the fault's signature.
→
3
Predict the spread
The early shape — a growing cluster on one node — is detected before most customers notice, and projected forward to flag the node at risk.
→
4
Prescribe the action
The layer names the node and the most likely cause (aggregation, line, transport) and routes the specific remediation to the right team.
THE OUTPUT THE OPERATOR RECEIVES
“Access node A-2741 degrading: 18 homes with rising freeze/re-tune events over 25 min, signature = local aggregation. Recommended: inspect aggregation port before complaints escalate.”
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 8
Notes: UC1 mechanism. Four steps: stream and baseline; find the shared structure (co-movement on one node/path = signature); predict the spread before customers notice; prescribe the action naming the node and cause. Output is the concrete deliverable an operator sees.

## Slide 8
USE CASE 2 — INDIVIDUAL CUSTOMERS
Predict a specific customer's degradation — and the action to prevent it
02
THE PROBLEM TODAY
Today a customer is only visible once they call. Their experience has usually been deteriorating for days — repeated re-tunes, buffering, reboots — but nothing flags it until frustration turns into a support call or a cancellation.
WHAT WE DELIVER
We score each household against its own baseline, detect an emerging degradation early, and recommend the specific action for that customer — a targeted fix, a proactive contact, or a pre-emptive dispatch.
DATA THIS USE CASE NEEDS, BY LAYER
Set-Top Box per-device events & errors
TODAY
Home / Router Wi-Fi quality, gateway
TODAY
Customer device → household mapping
TODAY
Geography to separate home vs. area
INTEG.
Access net to confirm it's home-specific
INTEG.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 9
Notes: UC2 overview — individual customers. The problem: a customer is only visible when they call, after days of silent decline. The promise: score each household against its own baseline, detect early, recommend the specific per-customer action.

## Slide 9
USE CASE 2 — HOW IT'S SOLVED
From a silent decline to a targeted, pre-emptive action
1
Baseline each household
Every household has its own normal. The layer scores deviation continuously, so a personal decline is visible even when the customer hasn't complained.
→
2
Confirm it's the home
The graph checks neighbours on the same node. If peers are fine, the cause is isolated to this household — not the network.
→
3
Predict the tipping point
Repeated re-tunes, buffering or reboot patterns are projected forward to estimate when experience will cross into churn-risk territory.
→
4
Prescribe per-customer
The layer recommends the specific action — push a config/firmware fix, proactive outreach, or a correctly-scoped visit — with the reasoning attached.
THE OUTPUT THE OPERATOR RECEIVES
“Household 4471829 trending to churn-risk in ~6 days: Wi-Fi degradation, home-isolated. Recommended: proactive contact + gateway reconfiguration; no truck roll needed.”
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 12
Notes: UC2 mechanism. Baseline each household; confirm it's the home by checking neighbours on the node; predict the tipping point into churn risk; prescribe per-customer. Output: a specific household, a time-to-churn estimate, and an action that often avoids a truck roll.

## Slide 10
USE CASE 3 — INVISIBLE FAULTS
Detect the faults today's tools miss — even after a set-top box swap
03
THE PROBLEM TODAY
Some persistent problems are never found: the logs carry no label for them, so current tooling sees nothing. The customer is told to restart or the box is swapped — and the fault returns, because it was never in the box.
WHAT WE DELIVER
Because we reason on structure and behaviour rather than on a single labelled error, we surface these hidden faults and place them in their true layer — home, access, core or content — ending the cycle of fruitless box swaps.
DATA THIS USE CASE NEEDS, BY LAYER
Set-Top Box behavioural patterns, not labels
TODAY
Home / Router in-home behaviour signals
TODAY
Customer recurrence across the household
TODAY
Topology to localize beyond the device
INTEG.
CDN / platform to catch content-source faults
INTEG.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 13
Notes: UC3 overview — invisible faults. Directly answers Future Space's point about problems that persist even after a box swap, and the MoM tension that pixelation may have no label. The promise: reason on structure and behaviour, not a single labelled error.

## Slide 11
USE CASE 3 — HOW IT'S SOLVED
Finding what has no label — and proving it isn't the box
1
Learn normal behaviour
Instead of waiting for a known error code, the layer learns each device and population's normal rhythm and flags structural deviations that carry no explicit label — the unlabelled pixelation case.
→
2
Test against the box
Recurrence is tracked across a swap: if a new set-top box shows the same signature, the box is exonerated and the fault lives elsewhere.
→
3
Localize the real cause
The shape on the graph places the hidden fault in its true layer — home wiring, access, core path, or a content source — rather than the endpoint.
→
4
Surface with evidence
The finding is raised as a certified diagnosis — claim, evidence, provenance — so a previously invisible, recurring fault becomes actionable.
THE OUTPUT THE OPERATOR RECEIVES
“Recurring impairment persists across STB replacement on 9 households — signature points to access-segment, not CPE. Recommended: investigate segment; stop dispatching box swaps.”
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 16
Notes: UC3 mechanism. Learn normal behaviour rather than waiting for a known error code; test against the box (same signature on a new STB exonerates the box); localize the real cause via path identity; surface with a certified diagnosis. Output: recurring impairment persisting across STB replacement — stop dispatching box swaps.

## Slide 12
WHAT WE NEED TO BEGIN
The data assumptions, and the next step
DELIVERABLE ON TODAY'S DATA
Set-top box events, home/router telemetry, and customer/household mapping are available now.
These already power per-customer scoring (UC2) and behavioural detection across box swaps (UC3) at their first level.
UNLOCKED BY INTEGRATION
Topology (device → access node) turns statistical localization into precise node attribution — the core of UC1.
Access, core and CDN/platform telemetry sharpen prediction and complete the picture for all three use cases.
Next step: a data-fields workshop with Telefónica. Confirm the exact fields available per layer — events, quality indicators, identifiers, topology — so each use case is scoped against real data and we start on what is deliverable today.
Donde el futuro se hace presente
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · 17
Notes: Close. Be explicit and honest about data. Deliverable today: STB, home/router, customer mapping — enough to start UC2 and UC3 at their first level. Unlocked by integration: the graph/path fields and topology (the UC1 core), then access/core/CDN/encoder. The concrete next step is a data-fields workshop with Telefónica to confirm exactly which fields exist per layer, with special focus on path identity and relationship fields.

## Slide 13
THE IRREDUCIBLE RECORD
SI runs on four fields, sampled every interval
In an IP network, Structural Intelligence needs only the flow record — source, destination, time, volume. Source and destination are an edge; time slots it into an interval; volume is the weight on that edge. That quadruple is the weighted graph-over-time. Everything else enriches and reports.
IP NETWORK · NetFlow / IPFIX
The proven analogy
source_addr origin of the edge
dest_addr target of the edge
timestamp which interval
bytes / packets weight on the edge
MOVISTAR · service graph
The same record, one type for every layer
entity_src STB / node / edge element
entity_dst its parent in the path
timestamp which interval
magnitude bytes OR impairment units
The one extension over NetFlow: the magnitude is emitted every interval even when it is zero — a flat healthy baseline is the reference a fault deviates from. Raw NetFlow is event-gated; the service graph needs a heartbeat.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · F1

## Slide 14
DATA REQUIREMENTS · BY LAYER
The same four fields, layer by layer
At each layer the variables fall into three groups: who/where on the graph (identity), the live signal we sample every interval (flow), and labels we add for the report (enrich). A few examples of each — not an exhaustive list.
Set-Top Box
IDENTITY
device_id household_id
FLOW
freeze_duration reboot_count startup_delay
ENRICH
error_code firmware_version
Home / Router & Wi-Fi
IDENTITY
gateway_id mesh_node
FLOW
wifi_snr wan_packet_loss wan_latency
ENRICH
pppoe_resets
Geography / Topology
IDENTITY
access_node_id olt_id upstream_node
FLOW
(defines the edges — no magnitude)
ENRICH
service_area_id
Access Network
IDENTITY
port_id line_id
FLOW
port_utilization line_snr fec_errors
ENRICH
optical_rx_power
Core Network
IDENTITY
route_id / ecmp_path
FLOW
transport_load path_latency queue_depth
ENRICH
jitter
CDN / Platform / Content
IDENTITY
cdn_edge_id content_id multicast_group_id
FLOW
segment_failures cache_hit_ratio encoder_dropped_frm
ENRICH
asset_type
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · R2

## Slide 15
INTEGRATION POINTS · OPTION 1
Offline architecture — no complex integrations
No integration into operational systems: just an export of data already stored on Telefónica's internal platform (CKBO ** confirmation needed **).
INSIDE TELEFÓNICA
CKBO
Historical data
(≈ 1 month, already consolidated)
Export
Anonymized datasets
(no personal data)
FUTURE SPACE CONTROLLED ENVIRONMENT
Structural Intelligence
Model over the service
graph
Results
Dashboards & reports
for Telefónica
export
← Delivery of reports and operational recommendations to Telefónica
Key message: no integration into operational systems — just an export of already-stored data. Fast start, minimal security friction, no licence cost.
FAST START
ANONYMIZED DATA
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N2

## Slide 16
INTEGRATION POINTS · THE PRINCIPLE
A single collection point — not STB by STB
Telemetry already converges inside Telefónica before it reaches us. We connect where it is already gathered — ideally a single point — accepting a small lag. SI runs on intervals, so a small lag has no impact.
ELEMENTS (MILLIONS)
Millions of STBs
events, reboots, QoE
Routers / homes
Wi-Fi, gateway, WAN
Access: OLT / DSLAM
line, ports
Core / BNG
load, routes, multicast
CDN / platform
cache, encoder
ALREADY CONCENTRATED IN TELEFÓNICA
STB platform
telemetry from EVERY STB already arrives here in real time — never box by box
OSS bus / network telemetry
SNMP/gNMI from access, core and CDN already aggregated
SINGLE COLLECTION POINT
Data platform / streaming bus (live CKBO-style)
normalized to 4 fields:
• entity_src
• entity_dst
• timestamp
• magnitude
Structural Intelligence
a single subscription; recomputes the graph each interval
Design principle: the minimum number of integration points. Ideally just one — the live data bus where everything already converges — with a small acceptable lag. One integration, one security review, one schema.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N3a

## Slide 17
INTEGRATION POINTS · SCENARIOS
One if already unified; two at most
How many integrations are needed depends only on whether STB and network telemetry are already unified into a single real-time stream. In no case do we integrate element by element.
IDEAL SCENARIO
1 integration point
If STB + network already coexist on a live data bus / platform.
• One subscription to the data bus (live CKBO-style)
• Covers STB, home, access, core and CDN at once
• Small lag, irrelevant to SI
Preferred — minimal friction
REALISTIC SCENARIO
2 integration points
If STB and network telemetry are not yet unified.
• Point 1: STB platform (the entire STB fleet)
• Point 2: OSS bus / network telemetry
• Never per element — just two concentrators
Realistic floor — still very contained
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N3b

## Slide 18
PILOT SCOPE
Use cases, data, duration and deliverables
OPTION 1
Offline PoC — on historical data
USE CASES
• STB/set-top box degradation (pixelation, dropouts)
• Optional: fixed broadband degradation
DATA REQUIRED
Per-entity telemetry sampled at intervals — quality KPIs + event rates
Topology / path identity + entity & time keys · ≈1 month · anonymized
• ≈ 1 month of history · anonymized
DURATION
• 4–8 weeks from data receipt (indicative)
OPTION 2
Integrated pilot — on-prem
USE CASES
• The same, on (near) real-time telemetry
• Basis to scale to more use cases
DATA REQUIRED
• Continuous telemetry per layer (STB→access→core→CDN)
• Deployment inside Telefónica
DURATION
• Pilot + integration window (indicative)
DELIVERABLES (BOTH OPTIONS)
Degradation-prediction accuracy report · lista de recomendaciones operativas · proposal for the next phase (production / real-time integration)
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N4

## Slide 19
SUCCESS & ENGAGEMENT MODEL
What we consider a successful pilot — and the cost
WHAT COUNTS AS A SUCCESSFUL OUTCOME?
✓
STB degradation prediction with demonstrable accuracy over the month of data.
✓
Useful lead time: flag the problem before the customer complains.
✓
Fault localization to its true layer (home / access / core / content).
✓
Actionable operational recommendations, validated with the Telefónica team.
ENGAGEMENT MODEL & COST
Opción 1 · PoC offline no licence cost
Effort focused on analysis and reporting. Goal: prove value fast and build confidence.
Option 2 · Integrated pilot / on-prem
Deployment & integration: ≈12–13 k€ (order of magnitude. Potential de scale a up to 200 k€/year with more use cases. Data stays inside Telefónica.
Indicative figures, to be confirmed once the final pilot scope is set.
Narrative: we're confident enough in the technology to start with a no-licence-cost PoC on existing data. If it proves value, we scale to the integrated pilot in production.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N5

## Slide 20
NEXT STEPS
From approval to deployment proposal
A clear, low-risk path, aligned with Telefónica's budget cycle.
1
Conceptual approval
Sign-off on the offline PoC (Option 1).
2
1-month dataset
Definition and delivery from CKBO, with a designated technical contact.
3
Pilot execution
4–8 weeks (indicative) on the data received.
4
Results + proposal
Results presentation and deployment proposal (Option 2) with an indicative annual figure.
Timing opportunity: the offline PoC can start immediately with this year's budget, while Option 2 is planned for next year's budget.
Movistar Service Intelligence Twin · Commercial in Confidence
Future Space SA · N6